## Slide 1: STEP Conversion Use Cases -Composites Model Based Definition
John V. Van Horn
Associate Technical Fellow
Date
Commercial Airplanes: Airplane Level Engineering Integration (ALEI)
Name of meeting here

## Slide 2: Multiple formatting
Boeing MBD Format – use of structured spec tree with geometrical sets, surfaces, parameters, and applied materials.
FiberSIM data – locked away data format.
CATIA V5 Composite Part Design Data – DS composites data format

## Slide 3: Boeing Composite MBD Format

## Slide 4: CATIA V5 Composite Part Design Format

## Slide 5: FiberSIM Data Format
Not natively exposed to spec tree. Embedded and hidden data.

## Slide 6: Current path to Composite STEP data translations
FiberSIM Data:
  Convert to Boeing MBD -> Convert to V5 CPD->Convert to STEP.
  Or use Siemens FiberSIM STEP Converter Module (Boeing does not have).
Boeing MBD Data:
  Convert to V5 CPD->Convert to STEP.
V5 CPD Data:
  Convert to STEP.

## Slide 7: Target
Ability to convert any of the composites data formats directly to STEP AP242 composites.
For Boeing MBD format, min requirement is to preserve the data strucuture (nested geometric set tree structure), materials, and KW parameters that define the engineering intent.

## Slide 8
8